## Slide 1
How the Smart Dressing Decides, and How It Learned To
each block says what that stage does; the labels on the arrows say what it hands on
HOW IT LEARNED WHAT TO LOOK FOR - done once, before use
WHAT IT DOES AT THE BEDSIDE - about twice a second
The Dressing
25 sensing pads sitting over the tube fixation
Distrust a Broken Reading
if the sensor drops out, hold the last level rather than say all is well
Cancel the Slow Drift
sweat and body heat move the reading over hours; only sudden change matters
Describe the Moment
how far each pad moved, how many moved together, and how deep
Decide What Is Happening
nothing, a touch, the dressing peeling, or the tube being pulled
Wait for Agreement
one odd moment is not an alarm; several in a row is
25 readings, about twice a second
a reading worth trusting
how much each pad changed
one description of that moment
how likely each of the four levels is
How serious it is, how risky, and where the patch is lifting
How Risky, 0 to 100
one number for the bedside trend chart
Recorded Behaviour
81 recordings of nine known things happening to the patch
The Same Removal and Description
so learning sees exactly what the bedside will see
Learn the Patterns
a decision-tree model, over every recording at once
Measure Honestly
judged only on recordings it never learned from
Check Before Release
the same numbers again, every test passing
what was learned
Measured on one round of bench recordings with a single patch mounting: every event was caught, at roughly eight false alarms an hour.