## Slide 1
PROJECT 2 · SMART EXTUBATION EARLY WARNING
How the Smart Dressing Learns,
and How It Decides
A 25-pad capacitive dressing that warns before an intubated patient pulls out their own breathing tube.
81
bench recordings, nine kinds of behaviour
every
real event caught in testing
~8
false alarms an hour, the price of catching them
Notes: The device, and the two questions this deck answers: how it is taught, and how it decides at the bedside.

## Slide 2
Learning from data
the patch is worn while nine known things happen to it, and what happened becomes the answer we teach
1
Record what happens
Nine kinds of activity, from lying still to a full pull. Eighty-one recordings in all.
2
Sort into four levels
Normal. Someone touching it. The dressing peeling. The tube being pulled.
3
Cancel the slow drift
Sweat and body heat move the reading over hours. Only a sudden change means something is happening.
4
Describe each moment
How far each of the 25 pads moved, how many moved together, and how deep.
A recording that does not lift as far as the design requires is set aside before it is allowed to teach anything.
Notes: Drift removal and the description of each moment are the two things the live system repeats exactly.

## Slide 3
How well it works
measured three ways, because each answers a different question
PER RECORDING
97.5%
of recordings judged correctly, 79 of 81. The honest range around that is 91 to 99 per cent.
PER REAL EVENT
100%
of real events caught, with the warning arriving about six seconds in. This is the number that matters clinically.
ALARM BURDEN
~8
false alarms an hour. Quieter settings exist, but every one of them misses a real event.
Every moment is judged by a model that never learned from its own recording.
Notes: Recording-level accuracy depends on clip length, so the episode figure is the clinical one.

## Slide 4
Before it is allowed out
nothing ships on a number nobody can reproduce
1
Write the numbers down
One report. It is the only place any figure may be quoted from, in a paper or on a slide.
2
Measure it all again
The same numbers must come out, and every automated check must still pass.
3
Seal the model
Stored with a fingerprint, so a swapped or damaged model is refused rather than quietly used.
If the numbers do not come out the same, the work is wrong - not the report.
Notes: This is the rule that stopped figures drifting away from the code that produced them.

## Slide 5
At the bedside
the same drift removal and the same description as during learning, twice a second
1
A reading arrives
All 25 pads, about twice a second.
2
Distrust a broken reading
If the sensor drops out, hold the last level rather than report that all is well.
3
Cancel the drift
Exactly as it was done while learning.
4
Describe the moment
Exactly the same description as while learning.
5
Decide what is happening
Too small to matter, a touch, peeling, or a pull - with a risk score alongside.
6
Wait for agreement
One odd moment is not an alarm. Several in a row is.
OUTPUT how serious it is · how risky · where the patch is lifting
Notes: Steps 3, 4 and 6 are the same code that produced the measured figures.

## Slide 6
What it cannot claim yet
stated up front, because a safety device is judged on what it cannot do
The patch does not lift as far as the design requires
Every recording falls short of the drop the specification calls for. The sensor is fine; the way it was fixed to the rig is not.
A sideways pull does not lift the patch at all
It reads like someone pressing on the dressing. Detachment in general is not yet demonstrated.
One patch, one mounting, one round of recordings
Nothing here shows the same figures would hold on a freshly applied dressing.
Every figure in this deck is reproduced by re-running the measurement, not copied from an earlier draft.
Notes: Leading with the limitations is the strongest thing a safety-device submission can do.