## Slide 1
1
LEARNING FROM DATA
2
WHAT THE MODEL SEES
3
HOW WELL IT WORKS
4
BEFORE IT IS ALLOWED OUT
5
THE MODEL THAT SHIPS
6
AT THE BEDSIDE
A RECORDING SESSION
S1
Record Known Behaviour
the patch is worn while nine known things happen to it, from lying still to a full pull; 81 recordings in all
S2
Sort into Four Levels
normal, someone touching it, the dressing peeling, the tube being pulled
STOP - set the recording aside
is the recording usable ?
S0
Check a New Recording
does the patch lift as far as the design says it should, before this recording is allowed to teach anything
S3
Remember Which Data This Came From
so the system can tell later whether the model still matches the data behind it
S4
Cancel the Slow Drift
sweat and body heat move the reading over hours; only a sudden change means something is happening
S5
Describe Each Moment
how far each of the 25 pads moved, how many moved together, and how deep
PER RECORDING
PER REAL EVENT
ALARM BURDEN
S6
Test on a Recording It Never Saw
learn from the other 80, then judge the one held back, and repeat for all 81
S8
Judge Every Moment Blind
each moment is scored by a model that never learned from its own recording
S10
Try Every Alarm Setting
how many agreeing moments before it sounds, and how long it keeps sounding
S7
How Often the Clip Is Called Right
79 of 81, and the honest range around that is 91 to 99 per cent
S9
How Many Real Events Are Caught
every one of them, and the warning comes about six seconds in
S11
Choose What a Ward Can Live With
catches every event, at the cost of roughly eight false alarms an hour
S12
Write the Measured Numbers Down
one report, and it is the only place any figure may be quoted from
STOP - then the work is wrong, not the report
same numbers, everything still passes ?
S13
Train the Model That Will Be Used
a gradient-boosted decision-tree model, learning from every recording at once
S14
Seal It
stored with a fingerprint, so a swapped or damaged model is refused rather than quietly used
S15
A Reading Arrives
all 25 pads, about twice a second
S16
Distrust a Broken Reading
if the sensor drops out, hold the last level rather than report that all is well
S17
Cancel the Drift
exactly as it was done while learning
S18
Describe the Moment
exactly the same description as while learning
S19
Decide What Is Happening
too small to matter, a touch, peeling, or a pull, with a risk score alongside
S20
Wait for Agreement
one odd moment is not an alarm; several in a row is
OUTPUT how serious it is, how risky, and where the patch is lifting
no
yes
at the same time
what the check found
how often a clip is right
how many events are caught
the chosen alarm setting
no
yes
How the Smart Dressing Learns, and How It Decides
each block says what that stage does; the labels on the arrows say what is handed to the next stage
At the bedside the drift is cancelled and each moment described exactly as it was during learning, which is why the measured figures describe what a ward would actually see.
Measured on one round of bench recordings with a single patch mounting. The patch does not yet lift as far as the design requires, and a sideways pull does not lift it at all.